EMF 		Exercise Class 8			Answers

Q1 		Side and axial view diagrams:

By symmetry, the magnetic field lines will form circular loops around the axis.   will be zero inside radius a because the enclosed current is zero.

For r between a and b:

Apply Ampere’s Law to a circular path of radius r:   and  are always

parallel, and the magnitude of the field, B,  is constant for the whole path.

So,

The enclosed current is given by the current density

multiplied by the area of the pipe within radius r:

Ienc  =  J((r2  -  (a2).

Therefore 		B(2(r)  = (0J((r2  -  (a2)

(				  	for a < r < b

For a < r < b:	  The line integral is the same as before:

But the enclosed current is now the total current flowing through the pipe:     Ienc  =  J((b2  -  (a2).

So 					for  r > b.

Sketch of B vs. radius:

Q2	Adopt a point of view such that the current flows directly out of the page.  This means that the y-	axis points out of the page.

Current flows outwards all along the x-axis.  The lines of point in the -x direction above the x-	axis and in the +x direction below it.  To see this, consider the current as being carried by lots of 	parallel wires and think about the field pattern produced by one wire (apply right hand rule).

Apply Ampere’s Law to a rectangular closed loop, sides  a and b, as shown:

Sides 1 and 3:	 and are parallel			(	  =  BdL

Equal contributions from the two sides 	(	total contribution = 2Ba

Sides 2 and 4:	 and  are perpendicular			(   =  0

Enclosed current  =  (current density)(length of the x-axis enclosed by the loop)  =  (a.

So		(	B  =  (0(/2.

	Note that  is independent of distance from the plate.

# Text boxes

X

Z

B

B

Dotted line = loop

for line integral

B

X

Y (outwards)

Z

Current flowing out of

page all along the x-axis

a

b

1

2

3

4

dL

AXIAL VIEW

SIDE VIEW

a

b

Circular lines of B

B  (outwards)

B  (inwards)

dL

B

r

Area = (r2 - (a2

a

b

B

r