## ELECTRIC AND MAGNETIC FIELDS

## ANSWERS TO  WEEK 4 ASSIGNMENT

Q1: (a)   Position 1: (-28.81, 0, 0)  pm	Position 2: (11.71, 11.71, 11.71) pm

Using the formula for the potential at distance r from a point charge, the values of the 
	potential at each of the two positions due to the -particle at (0,0,0) are

where r1  =  [(28.812 + (0)2 + (0)2]1/2  		= 28.81  pm

where r2  =  [(11.71)2 + (11.71)2 + (11.71)2]1/2  	= 20.28  pm

e  = 1.602 x 10-19  C 		(0  =  8.85 x 10-12   C2 N-1 m-2

So		V1  =  100 V	V2   =  142 V		V2  - V1  =  42 V

(b)	V2  > V1    we would need to do work on a positive charge to go from 1 to 2, but 				a negative charge would be pulled along by the field.  Therefore the electron loses

potential energy in moving to position 2.

Or: r2  is less than r1, so electron would be pulled in towards

the new position, so losing potential energy.

(c)	PE lost is U  =  (Charge)(Potential difference)  =  (e)(V)

U  =  42 eV  	or    	U  =  (42)(1.602 x 10-19)  =  6.73 x 10-18  J.

Q2	Infinite plane of surface charge

density 8 (C m-2 is in the x-y plane.

(a)	 is everwhere perpendicular to the plane
 	of charge.  So for positive values of z, 
 	is in the +z direction.

(b)	For negative values of z,  is in the -Z direction.

(c) 	a:  (0,0,2) cm     	b:  (0,0,5) cm

From the lecture notes, E  = (/(2(o)  and V(z) = -Ez

(  =  8 x 10-6 C m-2    and 	(o = 8.85 x 10-12 F m-1   	(    	E  =  4.52 x 105 N C-1 	
 								for both points (since E is independent of z)

V1  =  -4.52  x 105(2 x 10-2)  =  -9.04 x 103  V  =  -9.04 kV

V2  =  -4.52  x 105(5 x 10-2)  =  -2.26 x 104  V  =  -22.6 kV

- -2 mC is moved from a to b.

Work done is |W|  = |q((V)|  =  |(-2 x 10-3)(22.60 – 9.04) x 103|  =   27.1  Joules

(Note that b is further away from the plane than a, so a negative charge must be pushed 
along the electric field direction from a to b – i.e., work must be done on the charge.)

- -2 mC charge moved from (0,0,5) to (5,5,5). 

Work done = zero as change in z is zero.

Q3:	(a)  Charge is uniformly distributed over 
 
 	the surface

spherical symmetry

field pattern is as for a point

charge outside the sphere.

For  r > R:  	E  = 0

Inside the sphere, E must be zero, because 
 	a spherical Gaussian surface of radius < R encloses no charge.

For  r > R:

where Q = total charge on surface = 4(R2(  	(	.

Relationship between potential and electric field:

Taking V = 0 at r = , to find V at radius r we integrate along a radial path from  to r:

(i)	For r > R, we have:

.

We would need to push positive charge from
  	 to r against the field, so V(r) is positive.

At the surface of the shell,

(ii)	For r < R, we do not need to do any further 
 	work to move the charge in, because E = 0 
 	    = 0.

Therefore, V(r) is constant, with the same value 
 	as that at the surface.

(b)	At surface of shell, PE of point charge q is  	(q)(V at surface)

At radius 2R, the PE is		 	.

This amount of PE has been converted to KE

# Text boxes

30

12

~ 6 for method

~ 2 each for

the three correct answers

10 for a very clear answer

Mark on method + convincing demonstration

of an understanding of work and PE

r1

r2

8

35

+X

-X

+Z

-Z

+Y  (into page)

E

5

5

4 + 4

4

4

2

4

3

R

10 for diagram + explanation of the field pattern and expressions for E inside and outside

Diagram is essential

here

Deduct ~ 3 if E is given as non-zero inside.

35

10 for using correct relationship between the electric field and V.  Working out the magnitude and determining the sign afterwards.is the recommended method.

8 for a

good

sketch

7:

4 for method

and

3 for correct answer