# ELECTRIC AND MAGNETIC FIELDS

# ANSWERS TO WEEK 8 ASSIGNMENT

Q1	

A suitable co-ordinate system has N-S-E-W 
in the X-Y plane, as shown, with +z 	
representing upwards and -z downwards.

The magnetic field has two components,

in the -x direction and  in the -z 
direction.

The electron's velocity, ,  is in the -y direction.

The magnetic force on the electron is

has magnitude vBv, and, by the right hand rule, points along the +x axis (South).

has magnitude vBh, and, by the right hand rule, points along the -z axis (Down).

Therefore

Putting     	e  =  1.602 x 10-19  C     	Bv  = 1 x 10-4 T	 
		Bh  =  3 x 10-5 T       		v = 2 x 106 m s-1,

we get		  -(3.20 x 10-17)     +    (9.61 x 10-18) .

The magnitude is    F  =  [(-3.20 x 10-17)2   +  (9.61 x 10-18)2]1/2   =  3.34 x 10-17    Newtons.

The direction is upwards and northwards,

at an angle   to the horizontal, given by

tan  =  Fz/Fx  =  Bh/Bv  =  0.3

=   16.7o

Q2	As shown in the lectures, the electron travels in a circular path with radius r given by

.

Putting 	me  = 9.11 x 10-31  kg	e = 1.602 x 10-19 C
v = 107 m s-1 	B  =  3 x 10-4 T,

gives 	r  =  190  mm.

If the electron hits the screen having been deflected by 
	a distance x, as shown, then

r2  =  (r - x)2 + L2	(	x2  - 2rx  +  L2  =  0.

Therefore 	x  =  r  (  (r2  -  L2)1/2 .

Putting r  =  190 mm  and L  =  100 mm, we get

x  =  190 ( 162  mm	(	 x  =  28 mm or  352 mm.

The larger value corresponds to the opposite side of an 
	electron’s circular orbit, which it never reaches.  Therefore  x  =  28 mm.

Q3	(a)  In the lectures, we derived this 
	equation for the Hall potential for a 
	rectangular conductor of sides a and 
	b carrying current I:

	  (

The current density is 	    	and 	, the Hall electric field.

Therefore			so	.

	(b)	Copper:   RH  =  6 x 10-11  V m A-1 T-1. 

		(i)	=   1.04 x 1029  electrons m-3

		(ii)	(  =  8.9 x 103 kg m-3 			mCu = 1.06 x 10-25 kg.  

			(   No of Cu atoms/ cubic metre is  NCu  =     =  8.40 x 1028

Therefore each atom contributes    =  1.24  free electrons.

Q4	(a)  Consider the loop as seen from above.  Let the 
 	current flow as shown.  The contribution of a small 
 	element, dl, to the magnetic field at the centre, O, 
	is given by

The magnitude of is just dL because  and are perpendicular, and the 	magnitude of  is 1.

By the right hand rule, the direction of  is  perpendicular to the coil, pointing into
	the page.

Let  be a unit vector pointing into the page.    Then  .

To find the total field, we integrate around the length of the semicircular loop, i.e., from  	L = 0 to  L = r, to get

.

(b) 	Let  point into the paper.

The straight sections don’t contribute to because

their  and  vectors are parallel.

From the result of part (a), the field at O will have

two contributions.

Inner loop:

Outer loop:

Therefore		.

So			.

# Text boxes

8 for a good

diagram

with the

vectors clearly shown

25

N

S

E

W

UP

DOWN

Bv

Bh

v

X

Y

Z

6 for a correct

equation for the magnetic force on the electron

5 for working 
it out

3 + 3 for final magnitude

25

L

x

r

r

10 for finding

r correctly

10 for getting the geometry right

5 for the final answer

5 for using

this equation

25

b

a

10 for deriving this
(5 + 5 for method and correct derivation)

5

5

I

O

dL

25

5 for a good diagram showing the vectors

4 for getting something 
like this

4 for deriving the integral + 4 for solving it

I

O

R2

R1

4 for the 
method

4 for deriving the answer correctly