ELECTRIC AND MAGNETIC FIELDS

Answers to ASSIGNMENT 9

Q1	(a)	The magnitude of magnetic moment is	(  =  (Current)(Area)(Number of turns)

So, (  =  (2)(0.05)2(10)  =  0.05  A m2

(b)	The torque vector is       .

Its magnitude is 		(  =  (Bsin(.

Its direction is perpendicular to and .

Applying the right hand rule, we find 
		that ( is into the paper (in the -z direction).

(c)	The torque tends to align and , decreasing the angle (.  
		In equilibrium, ( = 0 with the magnitude of the torque also = 0.

(d)	If the coil is at an angle ( to the x-axis, and is rotated through an angle d(, then the 
		work done is

dW  =  (d(  =  (Bsin(.

To find the work done in rotating the dipole from (  =  0  to (  = 180o, we integrate 
		this from 0 to (.

So,

Q2 		Step 1: Draw diagram showing field pattern

By symmetry, the magnetic field lines will form circular loops around the axis.  
B  will be zero inside radius a because the enclosed current is zero.

# Step 2: Choose best path for the line integral

Use a circular path of radius r:   and are 
always parallel

(     = BdL

and the magnitude of the field, B,  is constant 
for the whole path, so we can take B outside the integral.

# Step 3:  Work out the line integral

This applies for a < r < b and for r > b as it depends on the geometry 
of the field pattern which is the same for both regions.

# Step 4: Find the enclosed current

a < r < b : 	Ienc is given by the current density multiplied

by the area of the pipe within radius r:

Ienc  =  J((r2  -  (a2).

r > b:		Ienc is now the total current flowing through 
			the pipe:     
						Ienc  =  J((b2  -  (a2).

Therefore 		B(2(r)  = (0J((r2  -  (a2)

Step 4: Equate the line integral to (oIenc		B(2(r)  = (0Ienc

(				  	for a < r < b

(					for  r > b.

Sketch of B vs. radius:

Note that B = 0 for r < a as a closed path in this region encloses no current.

Q3	(a)  Consider the loop as seen from above.  Let the 
 	current flow as shown.  The contribution of a small 
 	element, dl, to the magnetic field at the centre, O, 
	is given by

The magnitude of is just dL because  and are perpendicular, and the 	magnitude of  is 1.

By the right hand rule, the direction of  is  perpendicular to the coil, pointing into
	the page.

Let  be a unit vector pointing into the page.    Then  .

To find the total field, we integrate around the length of the semicircular loop, i.e., from  	L = 0 to  L = r, to get

.

(b) 	Let  point into the paper.

The straight sections don’t contribute to because

their  and  vectors are parallel.

From the result of part (a), the field at O will have

two contributions.

Inner loop:

Outer loop:

Therefore		.

So			.

# Text boxes

35

8

(

X

Y

(

coil seen edge-on

5

5

(

B

5

12

8 for method and 4 for correct answer

30

B  (inwards)

B  (outwards)

a

b

Circular lines of B

SIDE VIEW

AXIAL VIEW

6 for good diagram

showing field pattern

3 for some explanation of field pattern

6

3 for choosing and explaining the right path

3 for evaluating the integral

correctly

dL

B

r

6

3 each

Area = (r2 - (a2

6

3 each

a

b

B

r

3

~ 1 for each region

I

O

dL

25

5 for a good diagram showing the vectors

4 for getting something 
like this

4 for deriving the integral + 4 for solving it

I

O

R2

R1

4 for the 
method

4 for deriving the answer correctly