## ELECTRIC AND MAGNETIC FIELDS

## ASSIGNMENT 8

# All questions carry equal marks

Q1	At a particular location, the Earth's magnetic field has a vertical component (downwards) 	of  1 x 10-4 T, and a horizontal component (Northwards) of 3 x 10-5  T.  An electron in a TV tube

is moving East  West with speed 2 x 106 m s-1. Find the magnitude and direction of the

magnetic force on the electron.

Hint: 	Define an x, y, z co-ordinate system, and draw a diagram showing all the relevant 	vectors in terms of their components.  Use the equation for the magnetic force on a moving 	charged particle, being careful to apply the right hand rule and take the negative charge of 
	the electron into account.

Q2	A magnetic field is used to deflect a beam of

electrons before it strikes a screen.  The electrons, travelling at a speed  v, enter a region in which the magnetic field, B, is perpendicular to the direction of motion, as shown.   

As proved in the lectures, the path followed by the electrons is a circle of radius, r, given by	

		.

In a particular case,  v  =  107 m s-1, B  =  3 x 10-4  T, and L  = 100 mm.  Find the 	distance, x,  	from the centre of the screen to the point where the electrons strike. 	[Answer = 28 mm]

Q3	The Hall coefficient of a material is defined as  RH  = E/JB, where J is the current density 	(current 	per unit area) in the material, B is the magnitude of the externally applied magnetic field

perpendicular to the direction of the current, and E is the magnitude of the Hall electric field.

	(a)	Using the result derived in the lectures for the Hall voltage, show that  RH  = 1/(ne),
		where n is the volume number density of charge carriers and e is the electronic charge.

(b)	For copper, RH  =  6 x 10-11  V m A-1 T-1.  

		(i) 	Find the volume number density of free electrons.
		(ii)	The mass density of copper is 8.9 x 103 kg m-3 and the mass of a copper
			atom is 1.06 x 10-25 kg.  On average, how many free electrons does each
			atom contribute?

Q4	(a)  Use the Biot Savart Law, 

		  ,

to show that the magnetic field, B, at the

centre, O, of a semi-circular coil of radius R,

carrying a current I, as shown, is given by

where  is a unit vector perpendicular to the plane of the coil.

	In which direction does   point (into or out of the paper)?

(b)  A current loop consists of two semicircular

arcs of radii R1 and R2, and two perpendicular

sections as shown.  Show that the magnetic

field, B, at O is given by

.

# Text boxes

screen

Continued on other side

I

R

O

I

O

R2

R1